## Slide 1: RadarID
RADAR-BASED USER IDENTIFICATION IN SMART ENVIRONMENTS
TEAM 5
Francisco Gonçalves
Guilherme Santos
Hugo Rodrigues
João Gaspar
Ricardo Dias
Sérgio Correia
Supervised by Dr.ª Ana Rocha, Dr.º Samuel Silva
PECI 2023/2024

## Slide 2: System Overview
Primary Focuses:
User ID Modality
  Model Evaluation and Training
Secondary Focus:
Simple interface for a dashboard as a proof of concept for user adaptation

## Slide 3: User Identification Modality
Data Acquisition
Receives raw radar data (TLV packets), parses them, and extracts essential information: 3D position and velocity (Doppler) of moving targets.
Data Filtering
A sliding window is used to process the resulting information.
First step consists of filtering: remove some noise, namely by discarding targets with velocity <1e-5 m/s.
Feature Extraction
Extraction of features from filtered radar data:
  Matrix associated to the heat map for each data type (X, Y, Z, Doppler) versus the elapsed time
  Vertical concatenation of matrices
  Resulting matrix converted to greyscale image.
Subject Identification
Relies on a model for subject identification, which given a feature (greyscale image) outputs a user ID/name.
Model previously trained using Transfer Learning and a dataset corresponding to the subjects to be identified.

## Slide 4: Setup, Protocol and Participants
Participants:
Seven male subjects were involved in the study aged between 20 and 21 years.
Protocol:
Three distinct trajectories, each aligned with the radar orientation:
  Parallel
  Mixed (Perpendicular, diagonal & parallel)
  Perpendicular

## Slide 5: Evaluation Approach
Transfer Learning:
  We used Transfer Learning by retraining the final layers of a pre-trained image classification model with our dataset, obtained by extracting features from the acquired radar data
  Pre-trained Model: MobileNetV2
  Same parameters as in previous group work at IEETA
Cross-Validation:
  Stratified 10-fold cross-validation
    In each iteration, 80% of the data used for training, 10% for validation, and 10% for testing.
Performance Metrics:
  Balanced Accuracy
  Weighted Average F1 Score

## Slide 6: Results for 7 ID's
Participants: Seven subjects
Trajectories:
Parallel
Mixed (Perpendicular, diagonal & parallel)
Perpendicular
Figure 1: F1 score for each subject performing all 3 trajectories

## Slide 7: Adaptation to the User (Dashboard)

## Slide 8: Conclusions
Proposed and developed a solution exploring radar data to test its applicability for user identification.
Explored the application of ML and TL techniques to comply with low data scenarios.
Implementing a demonstrator consisting of a simple interface that adapts to the current identified user.
The obtained results (with an accuracy ranging from 70.8% to 94.4%) show the potential of using radar data together with machine/transfer learning techniques to perform subject identification in smart environments.
Although different challenges remain, our study already provides relevant and useful information that informs future research.